## Slide 1: Vector Programming
David Gregg
Trinity College Dublin

## Slide 2: Vector Parallel Computing
Vector computers
  One of the most powerful type of early supercomputers
  SIMD model
    One instruction performs the same operations on a whole bunch of data
Mathematicians call a 1D array a vector
  Vector instructions operate on 1D array
  Usually a short subsequence at a time
  Operations on 2D arrays built from 1D primitives

## Slide 3: Vector Extensions
Many processor designers have added a vector unit to their existing processors
  Intel
    Multimedia Extensions (MMX)
    Streaming SIMD Extensions (SSE)
    Advanced Vector Extensions (AVX)
      256 and 512 bit variants
  ARM
    NEON, SVE
  RISC V
    “V”

## Slide 4: Vector Architectures
Vector architectures are a type of SIMD
Registers contain a short array of values
  Intel SSE: 128 bits, four FP32 numbers
  Intel AVX: 256 bits, eight FP32 numbers
  Intel AVX512: 512 bits, 16 FP32 numbers
Vector machine instructions operate on all “lanes” of a vector instruction

## Slide 5: SSE
We are going to look at SSE
It’s quite old but…
  It’s supported on our lab machine
  It’s very similar to more recent, wider Intel vector instruction sets
Streaming SIMD extension (SSE)
  It’s just a brand name that’s supposed to sound high-tech
    “Flux capacitor”
    “Millennium Falcon”
    “Pan galactic gargle blaster”
  It’s a plain old short vector architecture

## Slide 6: Programming Vector Machines
There are several ways to program a vector machine
Program in plain C
  And hope that a heroic compiler will “vectorize” the code
  Production compilers are getting better
    Intel compiler is good
    GCC is okay
    LLVM is not good but improving quickly

## Slide 7: Programming Vector Machines in C
Two big problems for compiler automatic vectorization
  Pointers
  Data layouts

## Slide 8: Programming Vector Machines in C
Pointers
  void sum(float *a, float * b, float *c) {
  for ( int i = 0; i < N; i++ )
  a[i] = b[i] + c[i];
  }
  In general the compiler has no idea whether pointers a, b, c point to the same memory
  Restrict pointers guarantee not to point to same memory as another restrict pointer
  void sum(float * restrict a, float * restrict b, float * restrict c);

## Slide 9: Programming Vector Machines in C
Data layout is often crucial to the vectorization of code
  struct point {
  float x, y, z;
  };
  struct point my_points[1024];
  As compared to…
  struct points {
  float x[1024], y[1024], z[1024];
  };

## Slide 10: Other Approaches to Programming Vector Machines
Program in a domain-specific language
  Aimed at vector types
  Often obscure languages
    “Mom and pop” languages
    Maintenance, legacy problems
More recently mainstream languages are starting to add vector features
  E.g. vector types in C source code using Clang/LLVM
  “parallel SIMD” in OpenMP

## Slide 11: Other Approaches to Programming Vector Machines
Assembly
  Gives complete control over the machine
  Can pick exactly the right vector instructions
  Tedious, error prone, hard to maintain
Compiler “intrinsics”
  Functions that are built into compiler
  Vector machine instructions are expressed as C function calls
  Middle ground between assembly and pure C

## Slide 12: Compiler Intrinsics
We will do vector programming using compiler intrinsics
It’s sort of low-level, but we want to understand the architectures

## Slide 13: Vector Load Instructions
__m128 _mm_load_ps(float * src);
Load 4 floats from a 16-byte aligned address
__m128 _mm_loadu_ps(float * src);
Load 4 floats from a (possibly) unaligned address; slightly slower than aligned instruction
__m128 _mm_load1_ps(float * src);
Load one float into all four lanes of a vector
__m128 _mm_setr_ps(float a, float b, float c, float d);
Insert four values into four lanes of a vector
__m128 _mm_set1_ps(float a);
Insert a single value into all four lanes of a vector

## Slide 14: Vector Store Instructions
void _mm_store_ps(float * dest __m128 value);
Store a vector of floats to a 16-byte aligned address
Segmentation fault if the address is not aligned
void _mm_storeu_ps(float * dest, __m128 value);
Store a vector of floats to a 16-byte unaligned address
void _mm_store_ss(float * dest __m128 value);
Store the float value in lane zero to memory
There also exists:
__m128 _mm_load_ss(float * src)
Load a single float to lane zero of the destination vector; set other lanes to zero

## Slide 15: Arithmetic Instructions
__m128 _mm_add_ps(__m128 a, __m128 b);
Add corresponding lanes of a and b, and return a vector result
__m128 _mm_sub_ps(__m128 a, __m128 b);
Subtract corresponding lanes of a and b, and return a vector result
__m128 _mm_mul_ps(__m128 a, __m128 b);
Multiply corresponding lanes of a and b, and return a vector result
__m128 _mm_div_ps(__m128 a, __m128 b);
Divide corresponding lanes of a and b, and return a vector result
__m128 _mm_sqrt_ps(__m128 a);
Return a vector containing the square root of each value

## Slide 16: Example
void sum(float * a, float * b, float * c) {
for ( int i = 0; i < 1024; i++ ) {
a[i] = b[i] + c[i];
}
}

## Slide 17: Example
void sum(float * restrict a, float * restrict b, float * restrict c) {
for ( int i = 0; i < 1024; i++ ) {
a[i] = b[i] + c[i];
}
}
This might be vectorized as:
void sum(float * a, float * b, float * c) {
for ( int i = 0; i < 1024; i = i+ 4 ) {
__m128 b4 = _mm_loadu_ps(&b[i]);
__m128 c4 = _mm_loadu_ps(&c[i]);
__m128 a4 = _mm_add_ps(b4, c4);
_mm_storeu_ps(&a[i], a4);
}
}

## Slide 18: Example
void sum(float * a, float * b, float * c, int size) {
for ( int i = 0; i < size; i++ ) {
a[i] = b[i] + c[i];
}
}

## Slide 19: Example
void sum(float * a, float * b, float * c, int size) {
for ( int i = 0; i < size; i++ ) {
a[i] = b[i+1] + c[i];
}
}

## Slide 20: Example
void sum(float * a, float * b, int size) {
for ( int i = 1; i < size; i++ ) {
a[i] = a[i-1] + b[i];
}
}

## Slide 21: Example
void sum(float * a, int size) {
for ( int i = 1; i < size; i++ ) {
a[i] = a[i-1];
}
}

## Slide 22: Example
void sum(float * a, float * b, int size) {
for ( int i = 4; i < size; i++ ) {
a[i] = a[i-4] + b[i];
}
}

## Slide 23: Operating Across Lanes
The examples we have seen so far have all involved arithmetic on values of
  The same lane
  But Different vectors
Sometimes you want to be able to mix values from different lanes
  Simplest (but slow) solution is to store a vector to a temporary array:
float temp[4];
_mm_store_ps(temp, my_vector);

## Slide 24: Example
float mean(float * a, int size) {
float sum = 0.0;
for ( int i = 0; i < size; i++ ) {
sum = sum + a[i];
}
return sum/(float)size;
}

## Slide 25: Operating Across Lanes
There is also a very small number of arithmetic instructions that operate across lanes
By far the most important is:
_m128 _mm_hadd_ps(_m128 a, _m128 b);
  Takes operand a: [a3, a2, a1, a0]
  Operand b: [b3, b2, b1, b0]
  Returns: [a3+a2, a1+a0, b3+b2, b1+b0]

## Slide 26: Operating Across Lanes
There is also a very small number of arithmetic instructions that operate across lanes
By far the most important is:
_m128 _mm_hadd_ps(_m128 a, _m128 b);
  Takes operand a: [a3, a2, a1, a0]
  Operand b: [b3, b2, b1, b0]
  Returns: [a3+a2, a1+a0, b3+b2, b1+b0]

## Slide 27: Example
float mean(float * a, int size) {
float sum = 0.0;
for ( int i = 0; i < size; i++ ) {
sum = sum + a[i];
}
return sum/(float)size;
}

## Slide 28: Operating Across Lanes
Vector “swizzles” can also operate across lanes
  Permute: re-orders lanes within a vector
    Note that when we talk about “permute” we typically allow an element to be repeated
    This is different from a permutation in the mathematical sense of a reordering of the same elements
  Blend: Select corresponding lanes from two vectors
  Shuffle: A combination of permutes and blends

## Slide 29: Vector Swizzles
There are *lots* of swizzle operations in most vector instruction sets
  Lots of restrictions and special cases
This may seem odd
  It’s much easier for programmers and compiler-writers to use a small number of general instructions
For example we might like:
  An arbitrary permute operation
    Permute(|a,b,c,d|) -> any permutation, e.g. |b,d,c,a|
  An arbitrary blend operation
    Blend(|a,b,c,d|, |x,y,z,w|) -> any lane-wise selection
    E.g. |a,y,z,d|

## Slide 30: Vector Permutation
Arbitrary permute instructions are expensive to implement
  E.g. Vector with four lanes
  Each of the four result lanes can be any of the four input lanes
  Total possible permutations is 44 = 256
  Or if we restrict ourselves to permutation in the mathematical sense that 4! =24 possibilities
To implement this instruction we need
  A circuit that can map any input lane to any output lane
  An operand that specifies which of the possible 256 permutations should be implemented in this case

## Slide 31: Vector Permutation
Permutation circuit
  For each output lane
    Select from any of the input lanes
    #lanes == N, bit-width of lane == B
    Circuit of at least O(BN) gates per output lane
      Using “log shifter” circuits
    Total circuit at least O(BN2) gates
    Bigger circuits are slower, and may need pipelining
    Lots of cross-wise interconnection
  For #lanes == 4, this is not a problem
  For #lanes == 32, this is a big problem
    Even if we restrict ourselves to strict permutations, 32! Is a large number

## Slide 32: Vector Permutation
Specifying which permutation
  For #lanes == N
  Number of possible permutations is NN
    E.g. N == 4, NN == 256 == 28
      Requires 1 byte to specify which permutation
    N == 8, NN == 16,777,216 = 224
      Requires 3 bytes to specify which permutation
    N == 16, NN == 1.845 × 1019 == 264
      Requires 8 bytes to specify which permutation
    N == 32, NN == 1.461 × 1048 == 2160
      Requires 20 bytes to specify which permutation

## Slide 33: Vector Swizzling
Several vector permutation instructions in real instruction sets
  But often restrictions to reduce
    Circuit complexity
    Instruction length

## Slide 34: Vector Swizzling
We will primarily use
  _m128 _mm_shuffle_ps(a, b, _MM_SHUFFLE(1, 0, 3, 2);
  Two input vectors:
    |a3, a2, a1, a0|
    |b3, b2, b1, b0|
  Creates output vector based on _MM_SHUFFLE
    Selects first two lanes of result from a, second two lanes from b
    In this example parameters are (1, 0, 3, 2)
    Output: |a1, a0, b3, b2|

## Slide 35: Example - Hadd
Create a sequence of vector instructions that replicates the behaviour of the _mm_hadd_ps instruction
result = _mm_hadd_ps(a, b);
Inputs: |a3, a2, a1, a0|, |b3, b2, b1, b0|
Outputs|a3+a2, a1+a0, b3+b2, b1+b0|

## Slide 36: Example – Complex Multiplication
struct complex {
float r; // real
float i; // imaginary
};
struct complex a[1024], b[1024], c[1024];
for ( int j = 0; j < 1024; j++ ) {
a.r = (b.r * c.r) – (b.i * c.i);
a.i = (b.r * c.i) + (b.i * c.r);
}

## Slide 37: Accessing Individual Lanes
Most vector instruction sets have some mechanism to insert/extract a value to/from an individual lane within a vector
E.g. in Intel SSE
  __m128i _mm_insert_epi32(__m128i a, int b, const int lane_no);
  Returns a vector that consists of the original vector a, but with lane number lane_no overwritten with the value of b.

## Slide 38: Accessing Individual Lanes
Also in Intel SSE
  int _mm_extract_epi32(__m128i a, const int lane_no);
  Returns the integer stored in lane lane_no
Strangely, there is no equivalent instruction in SSE for floating point numbers
  In other words you can move a value from the vector registers to the general-purpose registers
  You cannot move a value from the vector registers to a floating-point register

## Slide 39: Accessing Individual Lanes
In practice the lack of floating point insert/extract instructions means that loading/storing directly to a lane is a pain
union m128convert {
_m128 f4;
_m128i i4;
};
  _m128 r = (m128) _mm_insert_epi32((_m128i) a, *((int*)ptr), LANE_NUM);
  *((int*)p) = _mm_extract_epi32((_m128)a, LANE_NUM);

## Slide 40: Accessing Individual Lanes
union m128convert {
_m128 f4;
_m128i i4;
};
union i2fconvert { int i,float f; };
_m128 insert2lane(_m128 a, float value, int lane) {
}

## Slide 41: Accessing Individual Lanes
  We could also define some standard macros to load/store floating point values to individual lanes.
  #define LOAD_LANE_PS(out_vec, in_vec, addr, lane_no) \
  (out_vec) = (m128) _mm_insert_epi32((_m128i) (in_vec), *((int*)(addr)), (lane_no));
#define STORE_LANE_PS(vec, addr, lane_no) \
  *((int*)addr) = _mm_extract_epi32((_m128)vec, lane_no);

## Slide 42: Bitwise Operations
Like most vector instruction sets, SSE provides a variety of bitwise instructions
__m128 _mm_and_ps(__m128 a, __m128 b)
__m128 _mm_or_ps(__m128 a, __m128 b)
__m128 _mm_andnot_ps(__m128 a, __m128 b)
__m128 _mm_xor_ps(__m128 a, __m128 b)
Bitwise vector operations allow lots of bitwise parallelism
  E.g. union/intersection of bit vector sets

## Slide 43: Comparison Operators
We can compare corresponding lanes of pairs of vectors
__m128 _mm_cmpeq_ps(__m128 a, __m128 b); // =
__m128 _mm_cmplt_ps(__m128 a, __m128 b); // <
__m128 _mm_cmple_ps(__m128 a, __m128 b); // <=
__m128 _mm_cmpgt_ps(__m128 a, __m128 b); // >
__m128 _mm_cmpge_ps(__m128 a, __m128 b); // >=
__m128 _mm_cmpneq_ps(__m128 a, __m128 b); // !=
__m128 _mm_cmpnlt_ps(__m128 a, __m128 b); // !<
__m128 _mm_cmpnle_ps(__m128 a, __m128 b); // !<=
__m128 _mm_cmpngt_ps(__m128 a, __m128 b); // !>
__m128 _mm_cmpnge_ps(__m128 a, __m128 b); // !>=

## Slide 44: Comparison Operators
The result of a comparison operation is always a mask with values:
  Integer 0 in false lanes
  Integer -1 in true lanes
__m128 a = _mm_set_ps(0.0f, 1.0f, 2.0f, 3.0f);
__m128 b = _mm_set_ps(3.0f, 2.0f, 1.0f, 0.0f);
__m128 mask = _mm_cmpgt_ps(a, b);
// mask now has value [0, 0, -1, -1]

## Slide 45: Comparisons and masking
0/-1 masks can be used with bitwise ops
  Integer zero is 0000000000000
  Integer -1 is 1111111111111
These can be used to mask out values
for ( i = 0; i < 1024; i++ ) {
if ( a[i] < b[i] ) {
a[i] = 0.0;
}
}

## Slide 46: Comparisons and masking
Masking can be used to vectorize many loops containing if statements
  First compute both sides of the if statement
  Then select the correct result for each lane using masks
  E.g.
for ( i = 0; i < 1024; i++ ) {
if ( a[i] > b[i] )
c[i] = a[i];
else
c[i] = b[i];
}

## Slide 47: Comparisons and masking
SSE also allows us to convert a full-width vector mask to a bit-by-bit integer mask
  int _mm_movemask_ps(mask);
  Takes a mask of 0/-1 lanes and converts each lane to a single bit of a result integer
  For example
    Bitmask Meaning
    1111 Comparison True for all 4 floats
    0000 Comparison False for all 4 floats
    1100 Comparison True for first two floats
    1010 Comparison True for first and third floats

## Slide 48: Comparisons and masking
The movemask converts a vector mask to an integer
  Integer can be stored to summarize comparison
  Integer can be tested with if or switch statement
  For example
  _m128 vec_mask = _mm_gt_ps(a, b);
  int mask = _mm_movemask_ps(vec_mask);
  switch ( mask ) {
  case 0: // all false ….

## Slide 49: Comparisons and masking
Vectorize the following code
float min = a[0];
for (i=1; i < 1024; i++ ) {
if ( a[i] < min ) {
min = a[i];
}
}

## Slide 50: Max and Min
Finding the minimum or maximum of pairs of numbers is so common that most vector instruction sets provide instructions
_m128 _mm_max_ps(_m128 a, _m128 b);
_m128 _mm_max_ps(_m128 a, _m128 b);

## Slide 51: When can we vectorize?
We normally vectorize loops
  It’s possible to use vector operations outside loops
  But loops are the most common use
We normally vectorize array code
  A “vector” is a one-dimensional array
  Vector machines are aimed at array code

## Slide 52: When can we vectorize?
A key factor is data dependencies between iterations of the loop
for ( int i = 1; i < size; i++ )
a[i] = a[i-1] * b[i]
To compute a[i], we must already know the value of a[i-1]
Thus, we must compute a[i-1] before we compute a[i]
Thus, we cannot compute a[i] and a[i-1] at the same time
Thus, we cannot vectorize this loop in its current form
  And we probably can’t vectorize this loop at all

## Slide 53: When can we vectorize?
Here there are no data dependencies
void scale(float * vals, float factor ) {
for ( int i = 0; i < 1024; i++ )
vals[i] = vals[i] * factor;
}
But what about here?
float b[2000]; float * a = &b[1];
void add(float * a, float *b, float *c ) {
for ( int i = 0; i < 1024; i++ )
a[i] = b[i] + c[i];
}

## Slide 54: When can we vectorize?
We normally vectorize loops where:
  There is no data dependency between iterations, or
  We can remove data dependency between iterations, or
  The distance between data dependent iterations is more than the vectorization factor

## Slide 55: Pointer Aliasing in C
In C it can be difficult to determine if two pointers point to the same location memory
void add(float * a, float *b, float *c ) {
for ( int i = 0; i < 1024; i++ ) {
a[i] = b[i] + c[i];
}
}
What if a, b, and c are all the same array that is passed to the function?

## Slide 56: Pointer Aliasing in C
It is difficult for the compiler to know if two pointers point to the same object
  Compiler pointer alias analysis can help, but only in very simple cases
Also, two pointers may be different, but point to different parts of the same array
float a[1024];
float b = &(a[2]);
for ( int i = 0; i < 1022; i++ ) {
b[i] = a[i] + 17;
}

## Slide 57: Pointer Aliasing in C
In C the programmer can guarantee that arrays point to different pieces of memory
void add(float * restrict a, float * restrict b, float * restrict c ) {
for ( int i = 0; i < 1024; i++ ) {
a[i] = b[i] + c[i];
}
}
Within the scope of the “restrict” variable, the programmer guarantees that they will access that memory only using the pointer, or a value directly derived from the pointer, such as *(a+1).

## Slide 58: Pointer Aliasing in C
C also has a “strict pointer aliasing” rule
  The compiler is free to assume that pointers to “incompatible” types do not point to the same memory
void scale(float * a, int *b) {
for ( int i = 0; i < 1024; i++ ) {
a[i] = b[i] * 3.14159265357;
}
}
Float and int are “incompatible” in C, so the compiler can assume that a and b point to different pieces of memory

## Slide 59: Pointer Aliasing in C
Some older C code is not correct with respect to the strict pointer aliasing rule
For example:
int reinterpret_float_as_int_and_set_zero(float * num) {
int * p = (int *) num;
int result = *p;
*num = 0.0;
return result;
}
In this code, the compiler could execute “*num = 0.0” before doing “result = *p”, because the strict aliasing rules say p and num cannot point to the same memory because they have incompatible types

## Slide 60: Pointer Aliasing in C
Some older C code is not correct with respect to the strict pointer aliasing rule
For example:
int reinterpret_float_as_int_and_set_zero(float * num) {
int * p = (int *) num;
int result = *p;
*num = 0.0;
return result;
}
In this code, the compiler could execute “*num = 0.0” before doing “result = *p”, because the strict aliasing rules say p and num cannot point to the same memory because they have incompatible types